## Slide 1: Sound Cards and Serial Ports in Linux
Ion Todirel
5/1/2024

## Slide 2: Project

## Slide 3: Motivation
Scriptable query of sound cards and serial ports
Scriptable soundcard volume control and test
Reliable sound card and serial port search and mapping
Full unattended automation
Notes: Searching for sound cards is not easily scriptable
Volume control on a per channel setting is not possible with CLI tools
Testing volume control not easy to do with existing tools
Finding one of many sound cards with non-unique/empty descriptors
udev rules limited in a multi device world and require system modifications

## Slide 4: Capabilities
Enumerating sound cards
Enumerating serial ports
Sound card volume enumeration and control
Mapping serial ports to sound cards
Mapping sound cards to serial ports
Printing to stdout and to JSON
Search from command line or via a JSON configuration file

## Slide 5: Project Information
Github: https://github.com/iontodirel/find_devices
Written in: C++ 20
Build system: CMake
Package Manager: FetchContent, apt
License: MIT
Platforms: Linux
LOC: 3,800

## Slide 6: Scripting example

## Slide 7: Digirig Hardware
Digirig Mobile
HUB
USB SERIAL BRIDGE
AUDIO
CODEC
USB
USB
USB
RX
TX
RST
https://digirig.net/product/digirig-mobile/

## Slide 8: Configuration
{
"search_criteria": {
"port": {
"serial": "f6a69ba44567ec119b112342ef680de7"
}
},
"volume_control": {
"controls": [
{
"name": "Speaker",
"playback_value": "100",
"playback_value_test_max_error": "5"
},
{
"name": "Mic",
"playback_value": "40",
"capture_value": "40",
"playback_value_test_max_error": "5",
"capture_value_test_max_error": "5"
}
]
},
"search_mode": "port-siblings"
}
Configuration for finding a serial port, and a “sibling” sound card

## Slide 9: Basic Enumeration Scripting
Uses config.json to find sound cards and/or serial ports
Set the volume controls
Write results to
find_devices -c config.json -o out.json --no-stdout
$find_devices_output = Get-Content -Path out.json -Raw | ConvertFrom-Json $audio_devices_count = $find_devices_output.audio_devices.Count
$audio_device = $find_devices_output.audio_devices[0].plughw_id
$serial_ports_count = $find_devices_output.serial_ports.Count
$serial_port = $find_devices_output.serial_ports[0].name
CLI:
Parsing Output in PowerShell:

## Slide 10: Volume Test Scripting
find_devices -c config.json -o out.json --no-stdout --no-volume-control
--test-volume-control
CLI:
Parsing Output in Bash:
Uses config.json to find sound cards and/or serial ports
Tests all volume controls as set in the config.json
volume_control_test_result=$(jq -r .volume_control_test_result out.json)
if [ "$volume_control_test_result" != "success" ]; then
exit 1
fi

## Slide 11: Mix and match
{
"volume_control": {
"controls": [
{
"name": "Speaker,
"channels": [
{
"name": "Front Center",
"playback_value": "80"
}
},
{
"name": “Line",
"playback_value": "50",
"capture_value": "50",
"channels": [
{
"name": "Front Left",
"playback_value": “20"
},
{
"name": "Front Right",
"capture_value": “40",
}
}
]
}
}

## Slide 12: Other examples

## Slide 13: Many Other Examples
https://github.com/iontodirel/find_devices/blob/main/README.md#practical-examples

## Slide 14: API Design

## Slide 15: Audio API Design
struct audio_device_info
{
std::string hw_id;
std::string plughw_id;
int card_id = -1;
int device_id = -1;
std::string name;
std::string stream_name;
std::string description;
audio_device_type type = audio_device_type::uknown;
};
struct audio_device_channel
{
std::string name;
int volume = 0;
int volume_linearized = 0;
audio_device_type type = audio_device_type::uknown;
audio_device_channel_id id = audio_device_channel_id::none;
};
struct audio_device_volume_control
{
std::string name;
std::vector<audio_device_channel> channels;
};
struct audio_device_volume_info
{
audio_device_info audio_device;
std::vector<audio_device_volume_control> controls;
};
API Usage Example Runtime Information
std::vector<audio_device_info> get_audio_devices();
bool try_get_audio_device_volume(const audio_device_info& device, audio_device_volume& volume);
bool try_set_audio_device_volume(const audio_device_info& device,
const audio_device_volume_control& control, const audio_device_channel& channel)

## Slide 16: Serial Ports API Design
struct serial_port
{
std::string name;
std::string description;
std::string manufacturer;
std::string device_serial_number;
};
std::vector<serial_port> get_serial_ports();
API Usage Example
Runtime Information

## Slide 17: Mapping API Design
struct device_description
{
int bus_number = -1;
int device_number = -1;
std::string path;
std::string hw_path;
std::string id_vendor;
std::string id_product;
std::string product;
std::string manufacturer;
int topology_depth = -1;
};
bool try_get_device_description(const audio_device_info& d, device_description& device);
bool try_get_device_description(const serial_port& d, device_description& device);
std::vector<audio_device_info> get_audio_devices(const device_description& desc);
bool try_get_serial_port(const device_description& desc, serial_port& p);
std::vector<device_description> get_sibling_audio_devices(const device_description& desc);
std::vector<device_description> get_sibling_serial_ports(const device_description& desc);
API Usage Example Runtime Information

## Slide 18: Implementation

## Slide 19: Library Dependencies
libasaund2-dev – ALSA development library
libudev-dev – Linux udev development library
fmt – Formatting library, now part of C++20
nlohmann/json – JSON library
cxxopts – Command line parsing library

## Slide 20: Package Management
apt-get
  libasaund2-dev
  libudev-dev
CMake (FetchContent)
  fmt
  nlohmann/json
  cxxopts

## Slide 21: FetchContent in CMake
if (CMAKE_VERSION VERSION_GREATER_EQUAL "3.24.0")
cmake_policy(SET CMP0135 NEW)
endif()
include(FetchContent)
FetchContent_Declare(json URL https://github.com/nlohmann/json/releases/download/v3.11.2/json.tar.xz)
FetchContent_GetProperties(json)
if(NOT json_POPULATED)
FetchContent_Populate(json)
add_subdirectory(${json_SOURCE_DIR} ${json_BINARY_DIR} EXCLUDE_FROM_ALL)
endif()
target_link_libraries(find_devices PRIVATE nlohmann_json::nlohmann_json)

## Slide 22: Enumerating audio devices
#include <alsa/asoundlib.h>
int card_id = -1; while (true)
{
snd_card_next(&card_id);
snd_ctl_t* ctl_handle = nullptr;
snd_ctl_open(&ctl_handle, fmt::format("hw:{}", card_id).c_str(), 0);
while (true)
{
int device_id = -1;
snd_ctl_pcm_next_device(ctl_handle, &device_id);
snd_pcm_info_t* pcm_info = nullptr;
snd_pcm_info_set_device(pcm_info, device_id);
snd_pcm_info_set_subdevice(pcm_info, 0);
snd_pcm_info_set_stream(pcm_info, SND_PCM_STREAM_CAPTURE);
snd_ctl_pcm_info(ctl_handle, pcm_info);
char* name = nullptr;
snd_card_get_name(card_id, &name);
char* long_name = nullptr;
snd_card_get_longname(card_id, &long_name);
fmt::format("hw:{},{}", device.card_id, device.device_id);
}
}
hw:0
hw:0,1
USB PnP Sound Device
C-Media Electronics Inc. USB PnP Sound Device
Notes: this is what is like using ALSA, it’s a C API
SND_PCM_STREAM_CAPTURE

## Slide 23: Volume Controls
#include <alsa/asoundlib.h>
snd_mixer_t* handle;
snd_mixer_selem_id_t* sid;
snd_mixer_open(&handle, 0);
snd_mixer_attach(handle, ("hw:" + std::to_string(device.card_id)).c_str()));
snd_mixer_selem_register(handle, nullptr, nullptr);
snd_mixer_load(handle);
snd_mixer_selem_id_malloc(&sid);
snd_mixer_selem_id_set_index(sid, 0);
snd_mixer_elem_t* elem = nullptr;
for (elem = snd_mixer_first_elem(handle); elem; elem = snd_mixer_elem_next(elem))
{
snd_mixer_selem_get_id(elem, sid);
audio_device_volume_control volume_control;
const char* control_name = snd_mixer_selem_get_name(elem);
for (int channel_id = 0; channel_id <= SND_MIXER_SCHN_REAR_CENTER; channel_id++)
{
const char* channel_name = snd_mixer_selem_channel_name(channel_id);
long min = 0, max = 100, value = 0;
snd_mixer_selem_get_playback_volume_range(elem, &min, &max);
snd_mixer_selem_get_playback_volume(elem, channel_id, &value);
}
}
hw:0
Front Left
Speaker
Notes: As far as I know this isn’t possible to do in Windows.

## Slide 24: Enumerating Serial Ports
#include <libudev.h>
udev* udev = udev_new();
udev_enumerate_add_match_subsystem(enumerate, "tty");
udev_enumerate_scan_devices(enumerate);
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_list_entry* dev_list_entry;
udev_list_entry_foreach(dev_list_entry, devices)
{
const char* path = udev_list_entry_get_name(dev_list_entry);
udev_device* dev = udev_device_new_from_syspath(udev, path);
const char* devnode = udev_device_get_devnode(dev);
udev_device* usb_dev = udev_device_get_parent_with_subsystem_devtype(dev, "usb", "usb_device");
const char* manufacturer = udev_device_get_sysattr_value(usb_dev, "manufacturer");
const char* product = udev_device_get_sysattr_value(usb_dev, "product");
const char* serial = udev_device_get_sysattr_value(usb_dev, "serial"); }
/dev/ttyUSB0
f6a69ba44567ec119b112342ef680de7
Silicon Labs

## Slide 25: Mapping: Devices to udev
#include <libudev.h>
udev* udev = udev_new();
udev_enumerate* enumerate = udev_enumerate_new(udev);
udev_enumerate_add_match_subsystem(enumerate, "tty");
udev_enumerate_add_match_property(enumerate, "DEVNAME", p.name.c_str());
udev_enumerate_scan_devices(enumerate);
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_device* device = udev_device_new_from_syspath(udev, udev_list_entry_get_name(devices));
udev_device* usb_device = udev_device_get_parent_with_subsystem_devtype(device, "usb", "usb_device");
const char* syspath = udev_device_get_syspath(device);
const char* usb_syspath = udev_device_get_syspath(usb_device);
Serial port to device description
/dev/ttyUSB0
udev_enumerate_add_match_subsystem(enumerate, "sound");
udev_enumerate_add_match_sysname(enumerate, fmt::format("card{}", d.card_id).c_str());
Sound card to device description
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.2/1-4.1.2:1.0/ttyUSB0/tty/ttyUSB0
filter
card0

## Slide 26: Mapping: Serial Port to Sound Card
#include <libudev.h>
udev* udev = udev_new();
udev_device* dev = udev_device_new_from_syspath(udev, desc.path.c_str());
udev_device* usb_dev = udev_device_get_parent_with_subsystem_devtype(dev, "usb", "usb_device");
udev_device* parent_usb_dev = udev_device_get_parent_with_subsystem_devtype(usb_dev, "usb", "usb_device");
udev_enumerate* enumerate = udev_enumerate_new(udev);
udev_enumerate_add_match_parent(enumerate, parent_usb_dev);
udev_enumerate_add_match_subsystem(enumerate, "sound");
udev_enumerate_add_match_sysname(enumerate, "card*");
udev_list_entry* sibling_list_entry = nullptr;
udev_list_entry* devices = udev_enumerate_get_list_entry(enumerate);
udev_list_entry_foreach(sibling_list_entry, devices)
{
const char* path = udev_list_entry_get_name(sibling_list_entry);
udev_device* sibling_dev = udev_device_new_from_syspath(udev, path);
udev_device* sibling_usb_device=
udev_device_get_parent_with_subsystem_devtype(device, "usb", "usb_device");
}
Serial port device description to sound card mapping
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.2/1-4.1.2:1.0/ttyUSB0/tty/ttyUSB0
/sys/devices/pci0000:00/0000:00:14.0/usb1/1-4/1-4.1/1-4.1.1/1-4.1.1:1.0/sound/card2

## Slide 27: Pretty Printing
fmt::print(fmt::emphasis::bold, "{:>4})", i);
fmt::print(fmt::emphasis::bold | fg(fmt::color::chartreuse), " {}", d.first.audio_device.hw_id);
fmt::print(fmt::emphasis::bold | fmt::emphasis::italic | fg(fmt::color::rosy_brown), "{:>20}: ", "hwid");
fmt::print(fmt::emphasis::italic | fg(fmt::color::gray), "{}\n", d.first.audio_device.hw_id);
fmt library:
Windows Integrated Terminal:

## Slide 28: Command Line Parsing
std::map<std::string, option_handler> command_map =
{
{ "version", {"v,version", false, nullptr, [&](const cxxopts::ParseResult& result) { args.show_version = true; }}},
{ "disable-colors", {"disable-colors", false, nullptr, [&](const cxxopts::ParseResult& result) { args.disable_colors = result["disable-colors"].as<bool>(); }}},
{ "disable-file-write", {"disable-file-write", false, nullptr, [&](const cxxopts::ParseResult& result) { args.disable_write_file = result["disable-file-write"].as<bool>(); }}},
{ "port.bus", {"port.bus", true, cxxopts::value<int>(), [&](const cxxopts::ParseResult& result) {
try_parse_number(result["port.bus"].as<std::string>(), args.port_filter.bus);
}}},
}; cxxopts::Options options("", "");
cxxopts::OptionAdder option_group = options.allow_unrecognised_options().add_options();
for (const auto& command : command_map)
{
option_group(command.second.command_line_arg_name, "", command.second.type);
}
cxxopts::ParseResult result;
try
{
result = options.parse(argc, argv);
}
catch (const cxxopts::exceptions::incorrect_argument_type& e) {/*Error parsing command line*/ }
catch (const std::exception& e) {} for (const auto& command : command_map)
{
const std::string& key = command.first;
const std::function<void(const cxxopts::ParseResult&)>& handler = command.second.read_handler;
if (result.count(key) > 0)
{
handler(result);
}
}
Command line parsing using the cxxopts library
struct option_handler
{
std::string command_line_arg_name;
bool has_type = false;
std::shared_ptr<cxxopts::Value> type;
std::function<void(const cxxopts::ParseResult&)> read_handler;
};
option_handler

## Slide 29: Testing

## Slide 30: Hardware
6
5
4
3
2
1
7
8
9

## Slide 31: Hardware
A 7.1 channel sound card
{
"audio_devices": [
{
"card_id": "3",
"device_id": "0",
"plughw_id": "plughw:3,0",
"hw_id": "hw:3,0",
"name": "ICUSBAUDIO7D",
"description": "ICUSBAUDIO7D at usb-0000:00:14.0-3, full speed",
"type": "capture&playback",
"controls": [
{
"name": "Speaker",
"channels": [
{
"name": "Front Left",
"type": "playback",
"volume": "36",
"channel": "front_left"
},
{
"name": "Front Right",
"type": "playback",
"volume": "36",
"channel": "front_right"
},
{
"name": "Rear Left",
"type": "playback",
"volume": "36",
"channel": "rear_left"
},
{
"name": "Rear Right",
"type": "playback",
"volume": "36",
"channel": "rear_right"
},
{
"name": "Front Center",
"type": "playback",
"volume": "36",
"channel": "front_center"
},
{
"name": "Woofer",
"type": "playback",
"volume": "36",
"channel": "woofer"
},
{
"name": "Side Left",
"type": "playback",
"volume": "36",
"channel": "side_left"
},
{
"name": "Side Right",
"type": "playback",
"volume": "36",
"channel": "side_right"
}
]
},
{
"name": "Line",
"channels": [
{
"name": "Front Left",
"type": "playback",
"volume": "76",
"channel": "front_left"
},
{
"name": "Front Left",
"type": "capture",
"volume": "0",
"channel": "front_left"
},
{
"name": "Front Right",
"type": "playback",
"volume": "76",
"channel": "front_right"
},
{
"name": "Front Right",
"type": "capture",
"volume": "0",
"channel": "front_right"
}
]
},
{
"name": "Mic",
"channels": [
{
"name": "Front Left",
"type": "playback",
"volume": "76",
"channel": "front_left"
},
{
"name": "Front Left",
"type": "capture",
"volume": "100",
"channel": "front_left"
},
{
"name": "Front Right",
"type": "playback",
"volume": "76",
"channel": "front_right"
},
{
"name": "Front Right",
"type": "capture",
"volume": "100",
"channel": "front_right"
}
]
}
],
"bus_number": "1",
"device_number": "9",
"id_product": "0102",
"id_vendor": "0d8c",
"device_manufacturer": "",
"path": "/sys/devices/pci0000:00/0000:00:14.0/usb1/1-3/1-3:1.0/sound/card3",
"hw_path": "/sys/devices/pci0000:00/0000:00:14.0/usb1/1-3",
"product": "USB Sound Device ",
"topology_depth": "2"
}
]
}

## Slide 32: Usage in Docker & Running an APRS digipeater

## Slide 33: APRS Digipeater Station
No overlays

## Slide 34: APRS Digipeater Station
12V power supply
mini-computer
GPS receiver
soundcard
with PTT circuit
USB isolator
radio transceiver
Radio: Yaesu FT-2980R
Soundcard: Digirig
GPS receiver: u-blox NEO-M9N
Mini-Computer: Intel N95 based
Power supply: MEAN WELL LRS-150-12
hardware

## Slide 35: Hardware Architecture
radio
transceiver
TX
RX
PTT
sound
card
UART
bridge
line out
line in
Linux
Environment
USB
Audio class
5V system voltage
VHF antenna
GPS
USB
Serial Port
GPS antenna
12V
system voltage
Wi-Fi antenna
USB
Digirig
USB Sound Card
switch
SMA
SMA
SO-239
Mic
Speaker
USB
USB-C (power only)
USB
USB
USB
USB
USB
Serial Port

## Slide 36: Docker Compose
direwolfm:
env_file:
- ".env"
build:
context: .
dockerfile: ./direwolf/Dockerfile
image: "direwolf"
ports:
- "${MODEM0_AGWP_PORT}:${MODEM0_PRIV_AGWP_PORT}“ # exposing KISS and AGWP ports to the host
- "${MODEM0_KISS_PORT}:${MODEM0_PRIV_KISS_PORT}"
volumes:
# find_devices config can be changed without rebuilding
- ${MODEM0_FD_CONFIG_FILE_NAME}:${MODEM0_PRIV_FD_CONFIG_FILE_NAME}
- ${MODEM0_LOG_DIR}:${MODEM0_PRIV_LOG_DIR} # share volume with host, for logging, so Direwolf logs can be read on the host
- ${MODEM0_DW_CONFIG_FILE_NAME}:${MODEM0_PRIV_DW_CONFIG_FILE_NAME} # Direwolf config, can be changed without rebuilding
- ./settings.json:${MODEM0_PRIV_SETTINGS_FILE_NAME}
networks:
- direwolf_network
- db_network
privileged: true
labels:
- "autoheal=true"
depends_on:
- db
healthcheck:
test: ["CMD", "pwsh", "-ExecutionPolicy", "Bypass", "-File", "/healthcheck.ps1"]
interval: "10s" # the interval to to perform health check
start_period: "60s" # how long it takes to start the container
retries: 1 # how many times to retry until the container becomes unhealty
timeout: "30s" # how long until the health check completes
restart: always

## Slide 37: Docker Compose continued
autoheal:
env_file:
- .env
image: willfarrell/autoheal:latest
logging:
driver: "json-file"
options:
max-size: "10m"
max-file: "10"
tty: true
environment:
- AUTOHEAL_CONTAINER_LABEL=all
volumes:
- /var/run/docker.sock:/var/run/docker.sock
restart: always

## Slide 38: Dockerfile
FROM ubuntu:23.10
RUN apt-get update -y
RUN apt-get install -y alsa-tools alsa-utils gcc g++ make cmake libasound2-dev libudev-dev git jq mysql-client netcat-traditional wget sox bc
RUN git clone https://github.com/iontodirel/find_devices.git
WORKDIR /find_devices
RUN cmake .
RUN make -j 4
RUN mkdir /powershell
WORKDIR /powershell
RUN wget https://github.com/PowerShell/PowerShell/releases/download/v7.2.12/powershell-lts_7.2.12-1.deb_amd64.deb
RUN dpkg -i powershell-lts_7.2.12-1.deb_amd64.deb
RUN apt-get install -f
WORKDIR /
RUN git clone https://github.com/iontodirel/direwolf-experimental.git
WORKDIR /direwolf-experimental
RUN cmake .
RUN make -j 4
RUN make install
WORKDIR /
COPY ./direwolf/entrypoint.ps1 entrypoint.ps1
COPY ./common.ps1 common.ps1
COPY ./direwolf/healthcheck.ps1 healthcheck.ps1
RUN chmod +x entrypoint.ps1 healthcheck.ps1
CMD ["pwsh", "/entrypoint.ps1"]

## Slide 39: entrypoint.ps1
. ./common.ps1
$serial_port = Get-SerialPort-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
-find_devices_output_json_file $find_devices_internal_output_json_file_name
$audio_device = Get-AudioDevice-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
-find_devices_output_json_file $find_devices_internal_output_json_file_name
Set-AudioDeviceVolume-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
Test-SerialPort-ExitOnError -serial_port $serial_port
Test-AudioDevice-ExitOnError -audio_device $audio_device -soundcard_test_wav_file_name $soundcard_test_wav_file_name
Update-DirewolfConfigFile -file_path $direwolf_internal_config_working_file_name `
-audio_device $audio_device `
-ptt_serial_port $serial_port `
-callsign $callsign `
-modem_internal_agwp_port $modem_internal_agwp_port_number `
-modem_internal_kiss_port $modem_internal_kiss_port_number
& /usr/local/bin/direwolf -t 0 -a 10 -c $direwolf_internal_config_working_file_name -l $modem_internal_log_directory 2>&1 |
tee -a $modem_internal_log_directory/direwolf-stdout.log

## Slide 40: healthcheck.ps1
. ./common.ps1
$null = Get-SerialPort-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
-find_devices_output_json_file $find_devices_internal_output_json_file_name
$null = Get-AudioDevice-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
-find_devices_output_json_file $find_devices_internal_output_json_file_name
Test-AudioDeviceVolume2-ExitOnError -find_devices_config_file $find_devices_internal_config_file_name
-find_devices_utility $find_devices_file_name
Test-TcpConnection-ExitOnError -host_name $service_name -port_number $modem_internal_kiss_port_number
If any of the tests fail, the container becomes unhealthy and autoheal will restart it
Containers health check

## Slide 41: Direwolf configuration
# DO NOT CHANGE, it will automatically be replaced in the container by entrypoint.ps1
@ADEVICE plughw:0,0
# DO NOT CHANGE, it will automatically be replaced in the container by entrypoint.ps1
# replace PTT with your own serial port if needed,
# some devices like Signalink have VOX and don't need
# the PTT line, comment it if the case, but also update entrypoint.ps1
@PTT /dev/ttyXYZ RTS
ACHANNELS 1
CHANNEL 0
DTMF
MODEM 1200
# DO NOT CHANGE, it will automatically be replaced in the container by entrypoint.ps1
@MYCALL N0CALL
@AGWPORT 8000
@KISSPORT 8001
NOTE: Everything starting with @ is automatically substituted in entrypoint.ps1

## Slide 42: APRX configuration
@mycall N0CALL
@myloc lat 0000.00N lon 00000.00W
<aprsis>
@passcode 0000
@server rotate.aprs2.net
heartbeat-timeout 1m
</aprsis>
<interface>
@tcp-device 127.0.0.1 8001 KISS
callsign $mycall
tx-ok true
telem-to-is true
</interface>
<beacon>
beaconmode both
cycle-size 45m
beacon interface $mycall via WIDE1-1 symbol "I&" $myloc comment "Downtown Bellevue fill-in TX iGate (722d3)"
</beacon>
<digipeater>
transmitter $mycall
<source>
source $mycall
relay-type directonly
viscous-delay 5
</source>
</digipeater>
NOTE: Everything starting with @ is automatically substituted in entrypoint.ps1
digipeater

## Slide 43: Software Architecture
USB sound card
device
gpsd
Aprx
ALSA
TCP
TCP
KISS TNC
GPS
device
u-blox NEO-M9N
clients
Xastir
Digirig
Digipeater
hardware
USB
serial
PinPoint
find_devices
direwolf.conf
Direwolf
gps_util
aprx.conf
1
2
3
4
5
Direwolf Container
Aprx Container
USB
radio
configuration
configuration
exec
TCP
TCP
TCP
Alsa
IO
IO
IO
USB
USB
Linux
Intel N95
GPS Container
find_devices

## Slide 44: USB Soundcard HW Design

## Slide 45: USB Sound Card Types
Integrated USB to analog CODECs ex: TI PCM2903C
MCU/DSP to I2S and I2S CODEC ex: ST STM32F769
MCU PWM based implementation ex: NXP MIMXRT1062
USB to I2S bridge and I2S CODEC ex: Silicon Labs CP2615
USB Transceiver + FPGA + ADC/DAC ex: SMSC USB3317C

## Slide 46: USB Audio Codecs and I2S bridges
Texas Instruments PCM2900C
Texas Instruments PCM2902C
Texas Instruments PCM2903C
Texas Instruments PCM2912A
C-Media CM108
Silicon Labs CP2615
Microchip USB24913P
ST Micro STM32F411
Cirrus Logic CS4244
Cirrus Logic CS4245
Analog Devices AD74111
Maxim MAX9860
AKM AK4558
AKM AK4571
FTDI FT901

## Slide 47: Texas Instruments PCM2903C
USB 2.0
  Self-Powered
16-Bit Delta-Sigma ADC and DAC
  DAC: 32, 44.1, 48 kHz
  ADC: 8, 11.025, 16, 22.05, 32, 44.1, 48 kHz
THD+N = 0.01%
SNR = 89 dB
Dynamic Range = 89 dB
Single 3.3V Power Supply
Single-Ended Voltage Input
$8.57
Package
System diagram

## Slide 48: A TI PCM2903C based design
Soundcard PCB render

## Slide 49: A TI PCM2903C based design
USB Codec IC
3.3V Linear Reg
USB Connector
Low Pass Filter
Isolation Transformers
3.5mm Audio Jacks
Audio Switch
Logic Gate
Oscillator

## Slide 50: Layer 2 – Power Routing

## Slide 51: Layer 1, 3, 4: Ground Planes

## Slide 52: Layer 1, 3, 4: Ground Planes – Up close

## Slide 53: Layer 3: Ground Planes

## Slide 54: Layer Polygons
No GND connection to bottom layer

## Slide 55: Codec

## Slide 56: Low Pass Filter

## Slide 57: LTSpice filter simulation
Filter Response 10Hz – 150KHz
Filter Simulation
20KHz
10dB
2Vpp
55KHz
0dB
0.6Vpp
100KHz
-10dB
0.09Vpp